## Slide 1: Operating Theatre Ventilation
FSC(OT)
ADNAN RAMZAN

## Slide 2
Operation theater ventilation is a specialized HVAC (heating, ventilation, and air conditioning) system designed to control airborne contamination in a surgical suite, thereby reducing the risk of surgical site infections (SSIs).
It works by
filtering
pressurizing air,
providing a flow of clean, sterile air towards the surgical field
efficiently removing contaminated air from the room.

## Slide 3: Why is Ventilation So Crucial?
Goals:
Patient Safety: To reduce the risk of post-operative wound infections by controlling airborne bacteria and contaminants.
Comfort & Efficiency: To provide a comfortable environment (temperature, humidity) for the surgical team.
Cost-Effectiveness: A well-designed system lowers both infection rates and long-term operating costs.
Key Fact: A poor ventilation system can lead to unnecessary patient suffering and higher healthcare costs.

## Slide 4: What Does Operating Room Ventilation Do?
The air supply has four main functions:
Dilute Contamination: Fresh air dilutes airborne germs and particles.
Control Airflow: Prevents dirty air from less clean areas flowing into the sterile operating zone.
Provide Comfort: Controls temperature and humidity for the surgical team.
Remove Hazards: Helps remove and dilute waste anesthetic gases

## Slide 5: Types of Ventilation Systems
There are two main categories of ventilation systems used in operating theatres:
Mixing Ventilation
Parallel Flow Ventilation (often called Laminar Flow)
Notes: Laminar mean in the form of layers with out turbulance

## Slide 6
Mixing Ventilation
  The standard, older system.
  Supply air mixes rapidly with the room's existing air.
Parallel Flow Ventilation (often called Laminar Flow)
  The modern, ultra-clean system.
  Air flows in a steady, parallel stream without mixing.
Notes: Steady mean constant

## Slide 7: Mixing Ventilation
Air is supplied from diffusers in the ceiling.
The new air mixes with the old room air to dilute contaminants.
Disadvantages
Unstable Airflow: Air moves in an uncontrolled manner.
High Contamination: The area around the operating table can have twice the concentration of contaminants (like bacteria or anesthetic gases) compared to the rest of the room.
Inefficient: Not ideal for removing hazardous gases effectively

## Slide 8: Parallel Flow (Laminar) Ventilation
clean air flowing straight down over an operating table How it Works
A large bank of HEPA filters in the ceiling supplies ultra-clean air.
Air moves in a steady, parallel stream directly over the operating table, like a "curtain of clean air."
It pushes contaminants away from the sterile site and toward the floor for exhaust.

## Slide 9: Advantages:
Creates an Ultra-Clean Zone directly over the patient.
Dramatically reduces the risk of airborne infection.
Highly effective for critical surgeries like joint replacements.

## Slide 11: Challenge with Standards
Existing standards often focus only on:
  Number of air changes per hour.
  Particle concentration levels.
The Gap: These standards provide good baseline safety but don't directly guarantee a system that minimizes post-operative infections. The design must go beyond just meeting the standard.

## Slide 12: Summary
Ventilation is Key: It is the most important system for preventing surgical site infections.
Choose the Right System: Parallel (Laminar) Flow is superior to Mixing Ventilation for creating an ultra-clean environment.
Design Matters: Every piece of equipment, from lights to surfaces, must be designed for easy cleaning and sterilization.

## Slide 13
Maintenance is Safety: Regular, scheduled maintenance of ventilation and equipment is essential for patient and staff safety.
Think Beyond Standards: Good theatre design must aim for the lowest possible infection risk, not just compliance with minimum standards

## Slide 14: Infection Control: Operating Theatre Lights
The design and maintenance of lights are critical for infection control.
Design Must-Haves:
Smooth Surfaces: Minimal cracks, crevices, or visible screws where dust and germs can hide.
Easy to Clean: Surfaces must be easy to wipe down without needing harsh chemicals.
Sterilizable Handles: Handles must be designed for easy sterilization.
Why? Dust and debris on lights can fall into the open surgical wound.

## Slide 15: Maintenance of Equipment
6-Monthly Safety Checks: All parts of the light should be inspected every six months.
Battery Backup: A minimum 3-hour battery backup is standard.
Full Discharge Test: This test must be performed to ensure the lights can actually run for 3 hours during a power outage.
Proactive maintenance prevents equipment failure in the middle of a surgery.