## Slide 1: Factor Affecting Quantity and Intensity
Fsc RIT
Awais Hamza

## Slide 2: X-ray Quantity Overview
X-ray quantity = mAs-controlled
Represents total number of photons in the beam
Affects image density/exposure
Mainly controlled by mA × exposure time

## Slide 3: mA (Tube Current)
Directly proportional to x-ray quantity
Higher mA → more electrons → more photons
mA doubles → quantity doubles
Does not affect photon energy

## Slide 4: Exposure Time (s)
Longer time → more electrons travel → more photons produced
Direct linear relationship
Used to control motion blur (short time ↓ blur)

## Slide 5: mAs (Product of mA × Time)
Primary controller of quantity
mAs ↑ → quantity ↑ proportionally
Follows mAs Reciprocity Law
Key for maintaining consistent receptor exposure

## Slide 6: kVp (Indirect Effect on Quantity)
kVp ↑ → more electrons reach target → more interactions → quantity increases
Effect is non-linear (approx. kVp² rule)
Increases both quantity + energy

## Slide 7: Filtration & Generator Type
Filtration
Added Al removes low-energy photons → reduces quantity
Generator type
High-frequency generators produce more consistent output
Quantity ↑ slightly due to less ripple

## Slide 8: FACTORS AFFECTING X-RAY INTENSITY
Distance (Inverse Square Law)
Intensity ∝ 1 / distance². Distance doubles → intensity becomes 1/4
Distance halves → intensity becomes 4×. Critical for patient dose & receptor exposure

## Slide 9: kVp Effect on Intensity
Higher kVp → produces more penetrating photons
Increases energy and intensity at the detector
Approximately intensity ∝ kVp²

## Slide 10: Filtration
Added filtration absorbs low-energy photons → intensity decreases
Results in a harder (more penetrating) beam
Reduces patient skin dose
Collimation / Beam Size:
Smaller field size → intensity per area increases at the center (heel effect reduced)
Larger field → more scatter → reduces useful intensity at image receptor
Beam restriction improves contrast

## Slide 11: THERMIONIC EMISSION & CATHODE
Cathode of the X-ray Tube: Basic Structure
The cathode is the negative electrode of the x-ray tube.
Two main components:
  Filament(s): usually tungsten (W) coil, high melting point (3370°C).
  Focusing cup: made of molybdenum or nickel, negatively charged.
Primary functions:
  Provide electrons (via heating).
  Focus the electrons into a narrow beam toward the anode.

## Slide 12: Filament Heating
Filament is heated by low-voltage, high-current circuit.
Current: 3–5 A, Voltage: 10–12 V.
Heating the filament to 2200°C causes electrons to gain enough energy to escape the metal surface.
Higher filament current → higher temperature → more electrons available.

## Slide 13: Thermionic Emission
Thermionic emission: release of electrons from a metal surface when heated.
Tungsten atoms vibrate more at high temperature → outer-shell electrons gain energy → escape.
Requires low-voltage (filament circuit).
The number of electrons released is called space charge.

## Slide 14: Space Charge & Electron Cloud Formation
Released electrons form a cloud around the filament, called the space charge.
Space charge limits further electron emission at low kVp (space-charge effect).
Focusing cup helps shape this cloud into a narrow electron beam.
At high enough kVp, the electrostatic attraction overcomes the space charge →
electrons accelerate.

## Slide 15: Space-Charge Effect & Its Control
At low kVp, the negative electron cloud repels new electrons → limits emission.
The tube’s mA stabilization system compensates to maintain constant mA.
Above ~70 kVp → space-charge limited region ends, and emission becomes
saturation current.

## Slide 16: Focusing Cup Function
Negatively charged metal cup around filament.
Functions:
Narrows & directs the electron cloud.
Reduces beam divergence.
Creates a sharp, small focal spot on the anode.
Larger negative charge = tighter focusing.

## Slide 17: Acceleration of Electrons (kVp Role)
High voltage (kVp) between cathode and anode creates potential difference.
Electrons accelerate across tube at half the speed of light.
Higher kVp → higher electron kinetic energy → more energetic x-rays.
This step converts electrical energy → kinetic energy.

## Slide 18: Electron Interaction at the Anode
When electrons hit the anode target (tungsten-rhenium), two outcomes:
Bremsstrahlung radiation (major portion).
Characteristic radiation (minor portion, discrete energies).
Less than 1% of electron energy becomes x-rays.
99% converts to heat.

## Slide 19: Relation Between Thermionic Emission & X-ray Production
More thermionic emission → more electrons → more interactions → more x-ray photons produced.
Therefore, mA (filament current) directly controls:
Number of electrons released
Number of x-rays produced (beam quantity)
kVp controls the energy of these photons.

## Slide 20: X-ray Tube Current
Tube current = flow of electrons from cathode to anode.
Measured in mA (milliamperes).
Directly proportional to:
Number of electrons emitted
Number of photons produced
Image receptor exposure
Controlled by filament current and space-charge compensation circuits