## Slide 1: RIT
Fsc RIT
Awais Hamza

## Slide 2: Practical Aspects of X-rays
1. Radiation Safety Always minimize exposure using ALARA; wear lead protection and maintain proper distance/time/shielding.
2. Equipment Operation Ensure the X-ray unit is calibrated, warmed up, and operated strictly per manufacturer protocols.
3. Patient/Object Positioning Correct positioning ensures diagnostic accuracy and reduces repeat exposures.

## Slide 3: Practical Aspects of X-rays
4. X-ray Beam Quality & Filtration Use proper filtration to remove low-energy photons, improving beam quality and lowering skin dose.
5. Collimation Always restrict the beam to the area of interest to reduce scatter and improve image contrast.
6. Image Quality Optimization Balance kVp, mAs, SID, and grids to obtain clear images with minimal noise and motion blur.

## Slide 4: Practical Aspects of X-rays
7. Exposure Parameters Choose appropriate kVp for penetration and mAs for density based on body part thickness.
8. Image Processing Apply correct digital processing algorithms to enhance contrast, sharpness, and detail.
9. Dose Monitoring Track patient dose using DAP meters or dose reports; avoid unnecessary repeat exposures.
10. Pregnancy Consideration Screen for pregnancy before imaging; postpone or shield abdomen when possible.

## Slide 5: Practical Aspects of X-rays
11. Compliance & Regulations Follow local radiation protection laws, license requirements, and QA/QC standards.
12. NDT (Non-Destructive Testing) Industry Use X-rays inspect welds, metals, and industrial components without damaging the material.
13. X-ray Crystallography Uses X-ray diffraction to determine atomic and molecular structures in crystals.
14. Stay Informed Regularly update yourself with new protocols, technologies, and safety guidelines.

## Slide 6: TRIODE VALVE
1. Structure (Quick Points)
A vacuum tube with three electrodes: Cathode, Anode (Plate), and Control Grid.
Cathode emits electrons; grid controls electron flow; anode collects electrons.
Enclosed in an evacuated glass tube.
2. Operation (How It Works)
Cathode heated → emits electrons (thermionic emission).
Control grid voltage regulates electron flow to the anode.
Small change in grid voltage → large change in plate current → amplification.

## Slide 7: TRIODE VALVE
3. Applications
Early radio amplifiers.
Oscillators, audio amplifiers.
High-power RF transmitters.
Specialized scientific equipment.
4. Advantages
High voltage and power handling.
Good linearity for audio.
Resistant to radiation and electromagnetic pulses (EMP).

## Slide 8: SEMICONDUCTOR DEVICE
1. Structure
Made from semiconductor materials such as Silicon or Germanium.
PN-junction (diode) or NPN/PNP layered structure (transistor).No vacuum; solid-state device.
2. Operation
Electrical conduction controlled by charge carriers (electrons and holes).
In diodes: PN junction allows current in one direction.
In transistors: base/emitter voltage controls collector current → amplification or switching.

## Slide 9: SEMICONDUCTOR DEVICE
3. Applications
Computers, mobile phones, ICs.
Switching circuits, amplifiers, power supplies.
Digital electronics, sensors, medical devices.
4. Advantages
Very small, lightweight, robust. Low power consumption, no warm-up needed.
Long life and high reliability.
Can be integrated into microchips.