## Slide 1: Applied Science
Fsc Medical Technologies
Awais Hamza

## Slide 2: Removal of Permanent Hardness
Permanent hardness is caused by chlorides and sulfates of calcium and magnesium (CaCl₂, MgSO₄). It cannot be removed by simple boiling, so special methods are used.
Key Methods:
Washing Soda Method
Sodium Zeolite (Permutit) Process

## Slide 3: Washing Soda Method (Na₂CO₃)
How it works: When washing soda (sodium carbonate) is added, it reacts with calcium and magnesium ions to form insoluble carbonates, which settle out.
Reactions:
CaSO₄ + Na₂CO₃ → CaCO₃↓ + Na₂SO₄
MgCl₂ + Na₂CO₃ → MgCO₃↓ + 2NaCl
Result: Hardness-causing ions get removed as precipitates.

## Slide 4: Sodium Zeolite Process (Ion-Exchange Method)
Also called: Permutit process How it works: Water is passed through a tank filled with sodium zeolite (Na-Ze). The zeolite exchanges its Na⁺ ions with Ca²⁺ and Mg²⁺ in hard water.
Reactions:
Ca²⁺ + Na-Ze → Ca-Ze + 2Na⁺
Mg²⁺ + Na-Ze → Mg-Ze + 2Na⁺
Regeneration: Ca-Ze + 2NaCl → Na-Ze + CaCl₂

## Slide 5: Why Hard Water Is a Problem
Forms soap scum; reduces soap efficiency
Causes scale deposits in kettles, boilers, and pipes
Leads to clogging and reduced water flow
Increases fuel and electricity costs due to poor heating efficiency
Creates hard deposits on skin and clothes
Damages industrial machinery and turbines