## Slide 1: Triode
Fsc RIT
Awais Hamza

## Slide 2: Triode
Definition
A triode is a three-electrode vacuum tube used for amplification and switching
It controls electron flow using an electrostatic grid
Electrodes
Cathode
Control grid
Anode (plate)

## Slide 3: Construction of Triode
Enclosed in evacuated glass envelope
Contains:
  Heated cathode
  Control grid placed between cathode and anode
  Anode surrounding grid

## Slide 4: Main Parts of Triode
Cathode
Control Grid
Anode (Plate)
Heater (filament)
Vacuum envelope

## Slide 5: Cathode
Heated metal surface
Emits electrons by thermionic emission
Source of electron cloud

## Slide 6: Control Grid
Fine wire mesh placed close to cathode
Controls electron flow
Small voltage change → large current change
Key Function: Amplification

## Slide 7: Anode (Plate)
Positively charged electrode
Collects electrons
Produces output current

## Slide 8: Working Principle of Triode
Based on:
  Thermionic emission
  Electrostatic control of electrons
Grid voltage controls plate current

## Slide 9: Basic Working of Triode
Cathode heated → emits electrons
Anode attracts electrons
Control grid regulates electron flow
Output current flows through anode circuit

## Slide 10: Triode as an Amplifier
Principle
Small change in grid voltage produces large change in plate current
Amplifying Process
AC signal applied to control grid
Grid voltage fluctuates
Plate current varies proportionally
Output signal amplified across load resistor

## Slide 11: Voltage Amplification
Voltage Gain=Input Voltage/Output Voltage​
High gain due to grid’s proximity to cathode
Grid draws negligible current

## Slide 12: Triode as a Switch
Principle
Grid voltage controls ON and OFF states
Switching Operation
Grid negative → Cut-off → OFF
Grid positive → Conduction → ON
Used in digital and pulse circuits

## Slide 13: Triode Characteristic Curves
Graphical relationship between:
Plate current
Plate voltage
Grid voltage

## Slide 14: Plate (Anode) Characteristics
Plate current vs plate voltage
Each curve represents different grid voltage
Shows saturation and cut-off behavior

## Slide 15: Transfer Characteristics
Plate current vs grid voltage
Shows control efficiency of grid
Determines amplification factor

## Slide 16: Mutual Conductance (gm)
gm​=ΔVg/​ΔIp​​
Measure of amplification capability
Higher gm → better amplifier

## Slide 17: Operating Regions of Triode
Cut-off region
Linear (active) region
Saturation region
Cut-Off Region
Grid sufficiently negative
No plate current
Used in switch OFF state

## Slide 18: Linear (Active) Region
Plate current proportional to grid voltage
Used for amplification
Most important operating region

## Slide 19: Saturation Region
Maximum plate current
Further increase in voltage gives no increase in current
Used in switching ON state

## Slide 20: Applications of Triode
Audio signal amplification
Radio receivers
Oscillators
Voltage amplifiers
Switching circuits
Early computing systems

## Slide 21: Advantages of Triode
High amplification
Smooth signal control
Low noise
Fast response

## Slide 22: Limitations of Triode
Grid-plate capacitance
Limited high-frequency response
Replaced by transistors in modern electronics