## Slide 1: Disinfection & Sterilization
ADNAN RAMZAN
Doctors Institute of Medical & Emerging Science

## Slide 2: Disinfection
Process of killing the pathogenic or disease producing microorganism but not usually bacterial spores.
Disinfectant is a germicide, an agent which kills pathogenic or disease producing microorganisms but, not usually bacterial spores, e.g. phenol and lysol.

## Slide 3
A deodorant is an agent, which suppresses bad odours, e.g. lime, bleaching powder
Detergent is a cleaning agent—usually a chemical substance—that helps remove dirt, grease, and other impurities from surfaces
Antiseptic is an agent which prevents the growth of "microorganisms

## Slide 4: Types of Disinfection
Disinfection
Concurrent Disinfection
Terminal Disinfection
Prophylactic Disinfection

## Slide 5: Types of Disinfection
Concurrent disinfection:
disinfection of infectious material (e.g. stools urine contaminated linen) throughout the course of an illness:
prevents the dissemination or further spread of the disease agent
Terminal disinfection:
This is disinfection that is undertaken at the termination an illness. (e.g. after recovery or death of the patient).

## Slide 6
3. Prophylactic disinfection:
pro- (before)
phylax (guard or protector
prophylactic” literally means “protecting beforehand.”
preventative measure to stop the spread of disease by eliminating or reducing microorganisms before they can cause an infection
Boiling of water, washing hands with soap and water are examples.

## Slide 7: Preparing article for Disinfection
Sets are packed into drums, bundles or on trays, labeled.
The articles should be carefully arranged so that those needed first-are on top.
They must be loosely packed for steam to penetrate.
Drums or bins must have the perforations .
Opened Bundles should have a double wrapper of close-woven cloth or of paper.

## Slide 8: METHODS OF DISINFECTION AND STERILIZATION
Methods of Sterilization
Natural
Sunlight
Air
Machanical
Scrubbing
Filtration
Sedmentation
Dry heat
Physical
Moist heat
Chemical
Solid
Liquid
Gas

## Slide 9: Natural Methods
Natural Methods
The ultra-violet rays from sunlight have the effect of destroying a large number of bacteria
Blankets,
pillows,
mattress
are disinfected by sunlight. Care should be taken to turn the articles often to kill the microorganisms on both surfaces.

## Slide 10: Mechanical Methods
Scrubbing:
Hand washing is one of the important procedures of OT staff in order to control and prevent self-infection as well as cross infection. Scrubbing and washing the hands with soap and water removes the organisms mechanically.
2. Filtration:
In laboratories, fluids are sterilized by filtration.
3. Sedimentation:
It is used in the purification of water. By this method the suspending materials together with bacteria settles down in the bottom of liquid.

## Slide 11: Physical Methods
Hot air oven
Sterilizing of glassware including syringes is often done in hot air oven at 160°C for one hour, Spores as well as organisms are killed.
Rubber articles will not withstand this heat. This method is not efficient where heat has to penetrate as in dressing towels and gloves.

## Slide 12
Incineration:
In order to destroy all organisms, infected wound dressings. contaminated materials, garbage and other hospital wastage, etc. are burnt by incineration. The apparatus used for this complete burning is incinerator
Flaming:
This is used in sterilizing platinum loops in laboratory

## Slide 13: 2) Moist Heat
This is a reliable method and may be used for most articles.
The autoclave is a chamber with an outer jacket and a lid or door, which can be firmly clamped.
Steam is generated by heating water in a boiler or in the outer jacket. Air is evacuated from the chamber

## Slide 14
5. Then the steam is allowed to build up pressure, usually 15 to 20 lbs per square inches and is kept at that pressure for 15 to 30 minutes
Then the heat is turned off and the contents of the autoclave allowed to dry out.
They should be quite dry when removed from the autoclave

## Slide 15
Points to remember:
All articles should be clean and dry before packing. Any organic matter such as blood or pus prevents penetration of steam.
The holder in the drums must be open when placing into the autoclave and closed Immediately on taking them out.

## Slide 16
Bundles should be neither too large nor too tightly packed.
Steam should be able to penetrate to the center.
Rubber gloves cannot withstand high temperature and long sterilizing Autoclave them separately at 15 lbs pressure for 15 minutes.
To autoclave bottles of fluid, loosen the screw cops, evacuate the steam slowly

## Slide 17: General instruction for autoclaving
The articles being sterilized should withstand high temperature.
The wrapper and the container should allow penetration of the stearn into the article.
The inner chamber must not be too full
Bundles and drums must be packed looses.
Cans or jars must be opened and turned on their sides so that steam can easily penetrate the contents

## Slide 18
6. The temperature and pressure of the steam should be high enough to kill all the microorganisms including spores. The usual temperature is 121°C and the pressure is 1.05 kg/cm²
7. The destruction of a bacteria depends upon the length of time the articles are exposed to steam under pressure.
8. The minimum time is 30 minutes. If the pressure is increased the exposure time can be reduced.