## Slide 1: Radiography and Imaging Technology
Fsc RIT
Awais Hamza

## Slide 2: Introduction
Absorption and scattering are fundamental processes that occur when electromagnetic radiation, such as X-rays or light, interacts with matter.
These processes play a crucial role in:
Medical imaging
Industrial inspection
Atmospheric science
Absorption refers to the process by which the energy of an incoming photon is taken up by the atoms or molecules in a material.
The photon is absorbed, and its energy is transferred to the absorbing particles.

## Slide 3: ABSORPTION – Key Point
1. Energy Transfer: When a photon is absorbed, its energy may be used to excite electrons to higher energy levels or to initiate other processes within the absorbing material.
2. Material Specific: The probability of absorption depends on:
Type of material
Energy of incident photons
Different materials have different absorption characteristics at various energy levels.
3. Material Interaction: Absorption involves interactions between the electromagnetic wave and electrons in the absorbing material.
It is more pronounced when the energy of the incident photons matches the energy levels of the electrons.

## Slide 4: ABSORPTION – Beer-Lambert Law
4. Beer-Lambert Law: The attenuation of intensity with distance through a material due to absorption is described by the Beer-Lambert law.
The intensity (I) decreases exponentially
Depends on thickness (d) and absorption coefficient (μ)
I₀ = initial intensity

## Slide 5: SCATTERING – Definition
Definition: Scattering involves the redirection of the path of a photon without a change in energy.
The incident photon interacts with particles in the material but is not absorbed.
1. Directional Change: Scattering can occur in various directions, and scattered photons may be redirected at different angles.
2. Elastic and Inelastic Scattering:
Elastic scattering → energy remains same
Inelastic scattering → energy changes

## Slide 6: SCATTERING – Types
3. Rayleigh Scattering:
Elastic scattering
Occurs when particle size is smaller than wavelength
Responsible for blue color of sky
4. Compton Scattering:
Inelastic scattering
Change in energy and direction of photon
5. Dependence on Particle Size: Larger particles → more scattering
6. Multiple Scattering: Photon may undergo multiple scattering events, leading to a complex path.

## Slide 7: INTERACTION IN DIFFERENT MEDIA
Gas and Atmosphere: Absorption and scattering affect sunlight and sky color
Biological Tissues: X-rays partially absorbed and scattered → diagnostic images
Materials Inspection: Used to inspect integrity of materials

## Slide 8: FILTRATION – Definition & Purpose
Filtration: Process of selectively removing low-energy X-rays from the beam
Purpose:
Improve image quality
Reduce patient dose
Inherent Filtration:
From X-ray tube components
Glass/metal envelope
Collimator
Added Filtration:
Additional filters (e.g., aluminum)
Removes low-energy X-rays

## Slide 9: EFFECTS OF FILTRATION
Removes low-energy, less-penetrating X-rays
Produces harder (more penetrating) beam
Improves image quality
Reduces patient dose
Filtration Material:
Aluminum commonly used
Compensating Filters:
Used for uniform image density
Beam Hardening:
Increases average energy of beam