## Slide 1: PHYSIOTHERAPY TECHNIQUES I
FSC PT I
Dr Danish Nadeem

## Slide 2: Ultrasound therapy
Overview: - Ultrasound is a therapeutic modality used by physical therapists since the 1940s. - Applied using a round-headed wand or probe in direct contact with the patient’s skin. - Ultrasound gel is used on all surfaces of the head to reduce friction and assist in transmission. - Frequency range: about 0.8–3.0 MHz. - Therapeutic ultrasound is generated by ultrasonic waves.

## Slide 3: Ultrasound

## Slide 4: Ultrasound Generation & wave Transmission
The waves are generated by a piezoelectric effect caused by the vibration of crystals within the head of the wand/probe. Sound waves that pass through the skin cause a vibration or cavitation.

## Slide 5: Effects on Tissues
- This vibration can cause a deep heating locally though usually no sensation of heat will be felt by the patient. - In situations where a heating effect is not desirable, such a fresh injury with acute inflammation, the ultrasound can be pulsed rather than continuously transmitted.

## Slide 6: Continued
Tissue relaxation & Blood flow: Ultrasound can cause increases in tissue relaxation, local blood flow. Therapeutic uses: - Help reduce local swelling and chronic inflammation. - Promote bone fracture healing.

## Slide 7: Power Density
- Measured in watts/cm². - Can be adjusted depending on the desired effect. - Goal is where scar tissue breakdown occurs.

## Slide 8: Time & Method
3-5 minutes depending on the size of the area being treated. - probe motion*: - Should be in constant motion. - Should feel no discomfort. - Holding probe in one place: - Can cause discomfort. - Energy buildup can result in discomfort.

## Slide 9: Indications
- Tendinitis - Non-acute joint swelling - Muscle spasm - Break down of scar tissue

## Slide 10: Contraindications
- Directly on the abdomen of pregnant women - Over active epiphyseal regions (growth plates) in children - Over the spinal cord in the area of a laminectomy - Over the eyes, skull, or testes - Local malignancy, metal implants, vascular abnormalities